## Slide 1: Explanatory note “Practical guide for indoor workplace lighting” NBN EN 12464-1
IBE-BIV Seminar 28 September 2023
Wouter Wissink
MET DE STEUN VAN
AVEC LE SOUTIEN DU

## Slide 2: NBN EN 12464-1: Lighting of work places –Part 1: Indoor work places
2003
2011
Modifications:
Complementary requirements:
visual comfort
-reflections background
-walls and ceilings
-handling of calculation and measurement points in a room
-additional requirements relating to glare
2021
Herziening:
Aanvullende eisen m.b.t.
visueel comfort
-hogere lichtbehoefte eist
-aandacht menselijke visuele behoeften
-flikker en stroboscopische effecten
-eisen voor de verlichting van werkplekken
-technische ontwikkelingen van leds
-extra toelichting verblinding
-invloed licht op visuele prestaties & welzijn
Notes: Aanvullende eisen visueel comfort 2011:
-minimumeisen aan verlichtingsniveau in de rest van de ruimte naast het taakgebied en directe omgeving. Zoals aanbevelingen reflecties.
-aanbevelingen reflecties wanden en plafonds
-hanteren van reken en meetpunten in een ruimte
-aanvullende eisen met betrekking tot verblinding
Herziening 2021:
-extra advies lichtopbrengst indien de omgeving een hogere lichtbehoefte eist
-aandacht menselijke visuele behoeften
-flikker en stroboscopische effecten
-eisen voor de verlichting van werkplekken om alle visuele taken uit te kunnen voeren, zijn opgesteld in directe relatie met de ruimte waarin deze worden uitgevoerd.
-er is rekening gehouden met de technische ontwikkelingen van leds die inmiddels de belangrijkste lichtbron geworden zijn.

## Slide 3: NBN EN 12464-1: Lighting of work places –Part 1: Indoor work places
2003
2011
2021
Revision:
Complementary requirements:
visual comfort
Modifications:
Complementary requirements:
visual comfort
-reflections background
-walls and ceilings
-handling of calculation and measurement points in a room
-additional requirements relating to glare
-higher light requirements
-attention human visual needs
-flicker and stroboscopic effects
-requirements for workplace lighting
-additional explanation of glare
-influence of light on visual performance & well-being
Notes: Aanvullende eisen visueel comfort 2011:
-minimumeisen aan verlichtingsniveau in de rest van de ruimte naast het taakgebied en directe omgeving. Zoals aanbevelingen reflecties.
-aanbevelingen reflecties wanden en plafonds
-hanteren van reken en meetpunten in een ruimte
-aanvullende eisen met betrekking tot verblinding
Herziening 2021:
-extra advies lichtopbrengst indien de omgeving een hogere lichtbehoefte eist
-aandacht menselijke visuele behoeften
-flikker en stroboscopische effecten
-eisen voor de verlichting van werkplekken om alle visuele taken uit te kunnen voeren, zijn opgesteld in directe relatie met de ruimte waarin deze worden uitgevoerd.
-er is rekening gehouden met de technische ontwikkelingen van leds die inmiddels de belangrijkste lichtbron geworden zijn.

## Slide 4: Task area and light distribution within a space
Visual tasks
Min. 50cm around task area
Min. 3m around adjacent zone
Task or
Area of activity
directly adjacent
area
background
Work surfaces mostly simple: offices
Difficult with
  moving operations
  Horizontal, vertical or inclined surfaces

## Slide 5: NBN EN 12464-1: Lighting of work places –Part 1: Indoor work places
2003
2011
2021
Revision:
Complementary requirements:
visual comfort
Modifications:
Complementary requirements:
visual comfort
-reflections background
-walls and ceilings
-handling of calculation and measurement points in a room
-additional requirements relating to glare
-higher light requirements
-attention human visual needs
-flicker and stroboscopic effects
-requirements for workplace lighting
-additional explanation of glare
-influence of light on visual performance & well-being
Notes: Aanvullende eisen visueel comfort 2011:
-minimumeisen aan verlichtingsniveau in de rest van de ruimte naast het taakgebied en directe omgeving. Zoals aanbevelingen reflecties.
-aanbevelingen reflecties wanden en plafonds
-hanteren van reken en meetpunten in een ruimte
-aanvullende eisen met betrekking tot verblinding
Herziening 2021:
-extra advies lichtopbrengst indien de omgeving een hogere lichtbehoefte eist
-aandacht menselijke visuele behoeften
-flikker en stroboscopische effecten
-eisen voor de verlichting van werkplekken om alle visuele taken uit te kunnen voeren, zijn opgesteld in directe relatie met de ruimte waarin deze worden uitgevoerd.
-er is rekening gehouden met de technische ontwikkelingen van leds die inmiddels de belangrijkste lichtbron geworden zijn.

## Slide 6
INDUSTRIAL ACTIVITIES
Work surfaces mostly simple: offices
Difficult with
  moving operations
  Horizontal, vertical or inclined surfaces
Task area, only one well defined visual task
Area of activity, several tasks can be performed here

## Slide 7
OFFICE ENVIRONMENT
OTHER SPACES
Task area, only one well defined visual task
Area of activity, several tasks can be performed here

## Slide 8: Criteria for each activity
Visual performance
Visual comfort
Notes: Uo: gelijkmatigheid
Ra: kleurweergave index
RUGL: hinderlijke verblinding = Unified Glare Rating

## Slide 9: Practical example office application
High percentage of elderly: lighting intensity 1 step up
20 – 30 – 50 – 75 – 150 – 200 – 300 – 500 – 750 – 1000 – 1500 – 2000 – 3000 – 5000 Lux
Applied scale according to the standard
Notes: Em,z: te behouden cylindrische verlichtingssterkte

## Slide 10: Lighting of a space
More accent to visual comfort
  Vertical surfaces and ceiling affect how a space is perceived visually.
  The color of a surface strongly influences its reflection properties

## Slide 11: Light design
8 essential steps for the design process
Comprehensive maintenance factor section
Product independent/manufacturer
application-specific

## Slide 12: Flicker and stroscopic effect
Explanation of difference flickering & stroboscopic
Possible causes
Parameters for indication

## Slide 13: Evaluation and risk of glare
RUG-method: from 10 - 28
Lighting equipment configuration
Room characteristics
Perception position of users
RUG is calculated by table method
usually provided by lighting manufacturers provided

## Slide 14: Example setup table method
RUG table method does not work for:
Appliances asymmetric beam
Purely indirect component
Directional spotlights
Appliances very small or very large luminous surface area
H: distance height eyes and
mounting surface fixtures

## Slide 15: Last but not least…
Easy, translations FR/NL for brochures, specifications, mailings....
Essential definitions that can be referenced for

## Slide 16: Thank you
MET DE STEUN VAN
AVEC LE SOUTIEN DU